## Slide 1
CSIM603154 - Jaringan Komunikasi Data
Fakultas Ilmu Komputer UI
Principles of network applications &
Web and HTTP
Lecture 04: Application Layer (1/3)

## Slide 2: Lecture 04: Roadmap
Chapter 02:
2.1 Principles of network applications
2.2 Web and HTTP

## Slide 3: Some network apps
e-mail
web
text messaging
remote login
P2P file sharing
multi-user network games
streaming stored video (YouTube, Hulu, Netflix)
voice over IP (e.g., Skype)
real-time video conferencing
social networking
search
…
…

## Slide 4: Creating a network app
write programs that:
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
no need to write software for network-core devices
network-core devices do not run user applications
applications on end systems allows for rapid app development, propagation
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 5: Application architectures
possible structure of applications:
client-server
peer-to-peer (P2P)

## Slide 6: Client-server architecture
server:
always-on host
permanent IP address
data centers for scaling
clients:
communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
client/server

## Slide 7: P2P architecture
no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
  self scalability – new peers bring new service capacity, as well as new service demands
peers are intermittently connected and change IP addresses
  complex management
peer-peer

## Slide 8: Processes communicating
process: program running within a host
within same host, two processes communicate using inter-process communication (defined by OS)
processes in different hosts communicate by exchanging messages
client process: process that initiates communication
server process: process that waits to be contacted
aside: applications with P2P architectures have client processes & server processes
clients, servers

## Slide 9: Sockets
process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door to deliver message to socket at receiving process
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 10: Addressing processes
to receive messages, process must have identifier
host device has unique 32-bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
identifier includes both IP address and port numbers associated with process on host.
example port numbers:
  HTTP server: 80
  mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
  IP address: 128.119.245.12
  port number: 80
more shortly…
  A: no, many processes can be running on same host

## Slide 11: What transport service does an app need?
data integrity
some apps (e.g., file transfer, web transactions) require 100% reliable data transfer
other apps (e.g., audio) can tolerate some loss
timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
security
encryption, data integrity, …

## Slide 12: Transport service requirements: common apps
application
file transfer
e-mail
Web documents
real-time audio/video
stored audio/video
interactive games
text messaging
data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
throughput
elastic
elastic
elastic
audio: 5kbps-1Mbps
video:10kbps-5Mbps
same as above
few kbps up
elastic
time sensitive
no
no
no
yes, 100’s msec
yes, few secs
yes, 100’s msec
yes and no

## Slide 13: Internet transport protocols services
TCP service:
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum throughput guarantee, security
connection-oriented: setup required between client and server processes
UDP service:
unreliable data transfer between sending and receiving process
does not provide: reliability, flow control, congestion control, timing, throughput guarantee, security, or connection setup,
Q: why bother? Why is there a UDP?

## Slide 14: Internet apps: application, transport protocols
application
e-mail
remote terminal access
Web
file transfer
streaming multimedia
Internet telephony
application
layer protocol
SMTP [RFC 2821]
Telnet [RFC 854]
HTTP [RFC 2616]
FTP [RFC 959]
HTTP (e.g., YouTube), RTP [RFC 1889]
SIP, RTP, proprietary
(e.g., Skype)
underlying
transport protocol
TCP
TCP
TCP
TCP
TCP or UDP
TCP or UDP

## Slide 15: Securing TCP
TCP & UDP
no encryption
cleartext passwds sent into socket traverse Internet in cleartext
SSL
provides encrypted TCP connection
data integrity
end-point authentication
SSL is at app layer
Apps use SSL libraries, which “talk” to TCP
SSL socket API
  cleartext passwds sent into socket traverse Internet encrypted
  See Chapter 7

## Slide 16: Lecture 04: Roadmap
Chapter 02:
2.1 Principles of network applications
2.2 Web and HTTP

## Slide 17: Web and HTTP
First, a review…
web page consists of objects
object can be HTML file, JPEG image, Java applet, audio file,…
web page consists of base HTML-file which includes several referenced objects
each object is addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 18: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
PC running
Firefox browser
server
running
Apache Web
server
iphone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 19: HTTP overview (continued)
uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 20: HTTP connections
non-persistent HTTP
at most one object sent over TCP connection
  connection then closed
downloading multiple objects required multiple connections
persistent HTTP
multiple objects can be sent over single TCP connection between client, server

## Slide 21: Nonpersistent HTTP
Suppose user enters URL www.someSchool.edu/someDepartment/home.index
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80. “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(contains text,
references to 10
jpeg images)

## Slide 22: Nonpersistent HTTP (cont.)
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.
time

## Slide 23: Non-persistent HTTP: response time
RTT (definition): time for a small packet to travel from client to server and back
HTTP response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time
non-persistent HTTP response time =
  2RTT+ file transmission time
time to
transmit
file
initiate TCP
connection
RTT
request
file
RTT
file
received
time
time

## Slide 24: Persistent HTTP
non-persistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open parallel TCP connections to fetch referenced objects
persistent HTTP:
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects

## Slide 25: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
request line
(GET, POST,
HEAD commands)
header
lines
carriage return,
line feed at start
of line indicates
end of header lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Firefox/3.6.10\r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Accept-Charset: ISO-8859-1,utf-8;q=0.7\r\n
Keep-Alive: 115\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character

## Slide 26: HTTP request message: general format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~

## Slide 27: Uploading form input
POST method:
web page often includes form input
input is uploaded to server in entity body
URL method:
uses GET method
input is uploaded in URL field of request line:
www.somesite.com/animalsearch?monkeys&banana

## Slide 28: Method types
HTTP/1.0:
GET
POST
HEAD
  asks server to leave requested object out of response
HTTP/1.1:
GET, POST, HEAD
PUT
  uploads file in entity body to path specified in URL field
DELETE
  deletes file specified in the URL field

## Slide 29: HTTP response message
status line
(protocol
status code
status phrase)
header
lines
data, e.g.,
requested
HTML file
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n
Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n
ETag: "17dc6-a5c-bf716880"\r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n
Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...

## Slide 30: HTTP response status codes
200 OK
  request succeeded, requested object later in this msg
301 Moved Permanently
  requested object moved, new location specified later in this msg (Location:)
400 Bad Request
  request msg not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
status code appears in 1st line in server-to-client response message.
some sample codes:

## Slide 31: Review
What is
  Client-server
  Peer-to-peer
  TCP
  UDP
  Socket
  SSL
  http
  Post method
  Get method
  Put method
  Head method
  Delete method
  Http Non-persistent
  Http Persistent